## Slide 1: Identification and authentication of enterprise network users
He Yiming

## Slide 2: Introduce
The office network carries many critical service systems within an enterprise. If terminals are connected to the network, they can directly access the office network resources. As a result, the network may be attacked and internal data may be stolen by attackers with illegal intentions. How to ensure the compliance and legitimacy of user access network has long become the focus of the industry. Network access authentication technology is produced under such background.

## Slide 3: Introduce
There are many access authentication methods, but the following four are common on campus networks:
1. Port Based Network Access Control (802.1X) authentication.
2. Portal authentication.
3. Point-to-Point Protocol Over Ethernet (PPPoE) authentication.
4. IPoE authentication.
802.1X authentication and Portal authentication are most commonly used in enterprise office network scenarios. This PPT will explain 802.1X certification.

## Slide 4: 802.1X authentication system
The 802.1X authentication system is composed of three roles: requestor, authenticator and authentication server. In practical applications, the three correspond to the client, Network Access control device (NAS), and RADIUS Server.
The solicitor is the role played by the client. It requests access to the network and responds to request messages from the authenticator. Requesters must run software that complies with the 802.1X client standard.

## Slide 5: 802.1X authentication system
Authenticator, usually an access device such as a switch or an AP, encapsulates the authentication information received from the client into a RADIUS packet and forwards it to the RADIUS Server. At the same time, the authenticator parses the information received from the RADIUS Server and forwards it to the client. Authenticator devices have two types of ports: controlled ports and uncontrolled ports.

## Slide 6: 802.1X authentication system
The authentication server is usually a RADIUS server that implements authentication together with the authenticator. The authentication server stores the user name and password, as well as the corresponding authorization information. One server can provide authentication services for multiple authenticators, so that users can be centrally managed.

## Slide 7: 802.1X authentication state machine
When the port is not authenticated and the controlled port is open, only EAPOL packets and broadcast packets (DHCP,ARP) are allowed to pass through the port, and other service flows are not allowed to pass through the port.
After the authentication is successful, the controlled port is closed and the user's service flow can pass smoothly.

## Slide 8: Maintenance of authentication status
The authenticator can periodically request the client to re-authenticate at a configurable time. The re-authentication process is user-insensitive, that is, users do not need to re-enter their passwords.
Downline mode
1. The physical port is Down: remove and reinsert the network cable, power off, and disconnect the Wi-Fi.
2. The re-authentication fails or times out;
3, the user actively offline;
4. The NMS is forcibly offline.

## Slide 9: 802.1X Basic authentication protocol
Authentication information is transmitted by EAP protocol encapsulated in EAPoL format between the client and the authenticator. The authenticator transmits information to the authentication server through the RADIUS protocol.
EAPoL protocol
The 802.1x protocol defines a packet encapsulation format called EAPoL (EAP over LANs Extended Authentication Protocol) packets. It is used to transmit EAP packets between the client and the authentication system to allow EAP packets to be transmitted over the LAN.

## Slide 10: 802.1X Basic authentication protocol
The RADIUS protocol specifies how to transfer user information and accounting information between the NAS and the RADIUS server. The RADIUS server receives connection requests from users, completes authentication, and returns configuration information required for transferring services to users to the NAS.

## Slide 11
Thanks